## Slide 1: VERILOG-HDL
Sajid Gul Khawaja

## Slide 2: Dataflow Modeling
Shows flow of data using
  Expressions
  Operands
Rules:
  Left hand side must be declared as type “wire”
  ALWAYS use keyword assign before any expression.

## Slide 3: Behavioral Modeling
Uses high level constructs such as
  If/else, case, casex, casez
  for, while, repeat, forever
Rules:
  Left hand side must be declared as type “reg”
  Code must be enclosed within a procedural block
    always
    initial
  DO NOT use keyword assign inside a procedural block.

## Slide 4: Initial and always block
Digital Design of Signal Processing Systems, John Wiley & Sons by Dr. Shoab A. Khan

## Slide 5: Procedural Assignments
Blocking Assignment (=)
  Regular assignment
  Value is assigned immediately
Non-Blocking Assignment (<=)
  Used in procedural block having clock in its sensitivity list
  Assigns values in parallel once the end of block is reached

## Slide 6: Examples
always@(*) begin
a = 5;
b = a;
end
always@(posedge clk) begin
a <= 5;
b <= a;
end
a = ?
b = ?
a = ?
b = ?

## Slide 7: Template for inferring Physical Register (Asynchronous)
always@(posedge clk or negedge rst_n)
begin
if (!rst_n)
begin
RegA <= 0;
RegB <= 0;
end
else
begin
RegA <= data_in;
RegB <= RegA;
end
end
data_in
RegA
RegB
rst_n
rst_n

## Slide 8: System Tasks or Simulation Control Statements
$finish
  Finishes Simulation
$display(“Value is = %d”, out);
  % specifies position of data to be displayed
  d specifies display format of data
  Executes only once
$monitor(“Value is = %d”, out)
  % specifies position of data to be displayed
  d specifies display format of data
  Executes whenever value of out changes

## Slide 9: Module Instantiating
Top-most Module (Calling Module)
My_Design_1
Input port is defined as either reg or wire
Output port is defined as wire only
Output port is of type “wire” by default; it can be redefined as “reg”
Input port is of type “wire”
Module Calling_module(…..);
reg in;
wire out;
My_Design_1 uut (in, out);
endmodule

## Slide 10: Module Instantiating
module Calling_Module(input a, output c);
reg b;
wire c_t, d_t;
My_Design_1 uut (a, c_t);
My_Design_1 uut2 (b, d_t);
My_Design_2 uut3 (c_t, d_t, c);
.
.
endmodule
Top-most Module (Calling Module)
My_Design_1
My_Design_2
My_Design_1
uut, uut2 and uut3
User defined Object names for modules
c_t
d_t
c
b
a

## Slide 11: Module Instantiating
module Calling_Module(input a, b, output c);
wire c_t, d_t;
My_Design_1 uut (a, c_t);
My_Design_1 uut2 (b, d_t);
My_Design_2 uut3 (c_t, d_t, c);
.
.
endmodule
Top-most Module (Calling Module)
My_Design_1
My_Design_2
My_Design_1
uut, uut2 and uut3
User defined Object names for modules
c_t
d_t
c
b
a

## Slide 12: ANSI Style Module Instantiating
My_Design_1 uut (.in(a), .out(b));
“a” can be defined as ?
“b” can be defined as ?
Top-most Module (Calling Module)
My_Design_1
a
b
in
out

## Slide 13: Parameters
By default 32 bit, used as constants
Assigned value remains same within the module (as const int in c)
Its value can be updated from calling module

## Slide 14: Example
  module xyz(………);
  parameter N =10; //Defining N as 10
  input [N – 1: 0] in; //Defining N bit input and output
  output [N – 1: 0] out;
  .
  .
  .
  endmodule
Calling
Xyz #(.N(10)) obj (…….);

## Slide 15: Guide Lines For Coding in HDL

## Slide 16: Avoid Latches
Avoid Latches at all cost
  Complete all conditions when using if-else (or case statement)
  Or Make use of else or default
Digital Design of Signal Processing Systems, John Wiley & Sons by Dr. Shoab A. Khan

## Slide 17: Avoid Latches
Use default values
Digital Design of Signal Processing Systems, John Wiley & Sons by Dr. Shoab A. Khan

## Slide 18: Use of CORES
Use XILINX provided cores whenever possible
  Block/Distributed RAM in place of local memory
    Specify depth of memory in power of 2 to avoid unnecessary warnings
  DSP48 module for various multi-operand operations
  Math functions such as
    Division
    Square root
    Sin, cos etc.
Use of cores helps in simplifying and optimizing the overall design

## Slide 19: Non-Synthesizable Constructs (Majorly used in simulation)
Do not use non-synthesizable constructs while designing
Example constructs
  initial
  forever
  always
    (without sensitivity list)

## Slide 20: Avoid Combinational Feedback
Digital Design of Signal Processing Systems, John Wiley & Sons by Dr. Shoab A. Khan

## Slide 21: Placement of registers
Place physical register at the input and output of your overall design.
Can automatically help in reducing overall delay
Ensures complete synthesis

## Slide 22: Cross-Checks after Completion of Design
Synthesize your code
Check Area and Timing Analysis
Cross check your RTL schematics
Run implement design
  Translate
  Map
  Place and Route
Run post route simulation and cross check your logic

## Slide 23: Major Errors and warnings
Multi-driver Error:
  When a single variable is assigned values at multiple places (assign or procedural blocks)
Incomplete Sensitivity list
FF latch inferred
Can not mix blocking and non-blocking statements
Trimming XYZ variable
Constant value in a variable

## Slide 24: On board Diagnostics
Use Chipscope-Pro to debug code at run time
Provides
  Integrated Controller (ICON)
  Integrated Logic Analyzer (ILA)
  Virtual Input Output (VIO)
  Agilent Trace Core 2 (ATC2) etc.

## Slide 25: Designing Examples

## Slide 26: Example: Difference Equation
N – 1 specifies a delay of 1 sample.
Physical Delay in HDL-VERILOG is added using a physical Register

## Slide 27: Difference Equation-Figure
+
x
x[n]
y[n]
y[n - 1]
0.5

## Slide 28: Comparator
i0 | i1 | eq
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 29: HDL Code
module eq1( input i0, i1, output eq);
wire p0, p1;
assign eq = p0 | p1;
assign p0 = ~i0 & ~i1;
assign p1 = i0 & i1;
endmodule
module eq1( input i0, i1, output eq);
reg p0, p1, eq;
always@(*)
eq = p0 | p1;
always @(i0, i1)
begin
p0 = ~i0 & ~i1;
p1 = i0 & i1;
end
endmodule

## Slide 30: HDL Code
module eq1( input i0, i1, output eq);
wire p0, p1;
assign eq = p0 | p1;
assign p0 = ~i0 & ~i1;
assign p1 = i0 & i1;
endmodule
module eq1( input i0, i1, output eq);
reg p0, p1, eq;
always@(*)
eq = p0 | p1;
always @(i0, i1)
begin
p0 = ~i0 & ~i1;
p1 = i0 & i1;
end
endmodule

## Slide 31: System Level Design and Testing

## Slide 32
Simulation Takes up to 60-70% of the developers time
Digital Design of Signal Processing Systems, John Wiley & Sons by Dr. Shoab A. Khan

## Slide 33: Stimulus-Test Bench
Used for verification of a design by providing known data called test vectors and comparing the response.
The design (top-level module) is instantiated inside the test-bench
Constructs that are not synthesizable can be used in stimulus

## Slide 34: Testing RTL Design
Make a simulation model
Generate and give test vectors to both
Test against the model
Digital Design of Signal Processing Systems, John Wiley & Sons by Dr. Shoab A. Khan

## Slide 35: Testing Standards
Testing against specifications while making use of the known internal structure of the system.
Enables easy location of bug for quick fixing
Performed by the developer
A set of inputs is applied and the outputs are checked
  against the specification or
    expected output
No consideration to the inner details of the system
Digital Design of Signal Processing Systems, John Wiley & Sons by Dr. Shoab A. Khan

## Slide 36: Stimulus: A Guide Line
Stimulus is the top-most module
Has no ports
Instantiates modules for testing
Provide data as test vectors using “initial” block
Generate clock via “initial” or “always” block

## Slide 37: Stimulus Example Code
module stimulus();
reg [7:0] A, B, C, D;
wire [7:0] Out1, Out2;
reg clk;
Device_under_test obj (A, B, C, D, clk, Out1, Out2);
initial begin
clk = 0;
A = 0; B = 0; C = 0; D = 0;
#10
A = 9; B = 6; C = 4; D = 2;
…..
end
always
#5 clk = !clk;
Initial
$monitor(“Output 1 = %d, Output 2 = %d”, Out1, Out2;
endmodule
Stimulus:
Has no ports.
Make instance(s) of testing module.
Use Initial to provide test vectors for verification
Either use $monitor for displaying output or use waveform

## Slide 38: Stimulus Example Code
module stimulus();
reg [7:0] A, B, C, D;
wire [7:0] Out1, Out2;
reg clk;
Device_under_test obj (A, B, C, D, clk, Out1, Out2);
initial begin
clk = 0;
A = 0; B = 0; C = 0; D = 0;
#10
A = 9; B = 6; C = 4; D = 2;
…..
end
always
#5 clk = !clk;
endmodule
Some Rules:
Port list order Must be same as declare or use ANSI Style
Object Name (obj here) should be unique for each instance.
Reset the system before providing input data (in codes where necessary)
Generate clock where necessary

## Slide 39: NOTE:
These slides DO NOT cover the complete syntax covered in class lectures
For complete syntax study Chapter 2 from Dr. Shoabs book or study lecture slides “Lec_Chap2.ppt”